## Slide 1
Yeh Shun-Liang
International College of Semiconductor Technology
National Yang Ming Chiao Tung University
Weekly meeting

## Slide 2: Recent Progress
Rerun the Simulation Under 22nm ITRS process node
Clarify the power model for energy calculation
Auto Refresh & WUPR Comparison

## Slide 3: Power Model
Energy are divided into Command energy & Background energy
Command energy are calculated & extracted using CACTI-3DD
Background energy is being calculated using the HBM2E voltage and currents

## Slide 4: Power Model(Per Bank Level Controller)
Category | Energy Component | Formula
Command Energy | Total Activation Energy | Activation Energy (nJ/Access) × Number of Activations (nJ)
 | Total Precharge Energy | Precharge Energy (nJ/Access) × Number of Precharges (nJ)
 | Total Read Energy | Read Energy (nJ/Access) × Number of Reads (nJ)
 | Total Write Energy | Write Energy (nJ/Access) × Number of Writes (nJ)
 | Total Refresh Energy | (((VDD × IDD5B) + VPP × IPP5B)× nRFCCycles × Number of Refreshes × tCKns ) / 1000 (nJ)
Background Energy | Active Background Energy | ((VDD × IDD3N) + VPP × IPP3N)× ActiveCycles × tCKns ) / 1000 (nJ)
 | Idle Background Energy | ((VDD × IDD2N) + VPP × IPP2N)× IdleCycles × tCKns ) / 1000 (nJ)

## Slide 5: Power Model(Per Bank Level Controller)
Category | Description | Value
VDD | Core Supply voltage | 1.0(V)
VPP | Wordline Boost Voltage | 1.5(V)
IDD2N | Precharge Standby Current | 40(mA)
IDD3N | Active Standby Current | 55(mA)
IDD5B | Refresh Current | 250(mA)

## Slide 6: Finding Optimal Number of Subarrays
Simulation Configuration | 
DRAM Model | Proposed 3D-DRAM Model
Number of Banks | 64
Ideal Bandwidth | 2TB/s
Ideal Bandwidth per Core | 128GB/s
Name of Trace | Single Core Partial LLM Workload Trace
Number of Traces | 193881265
Number of Subarrays | 64,128,256,512,1024
Clock Frequency | 1Ghz
DRAM Technology Node | ITRS 22nm

## Slide 7: Timing Constraints Trend
Chart: Timing Constraints Trend Under Different number of Subarrays
| 64 | 128 | 256 | 512 | 1024
nRCD | 8 | 7 | 7 | 7 | 6
nRAS | 30 | 16 | 12 | 10 | 10
nRC | 52 | 24 | 15 | 12 | 12
nCAS | 5 | 6 | 8 | 13 | 23
nRP | 23 | 9 | 5 | 3 | 2
nRRD | 2 | 3 | 3 | 3 | 4

## Slide 8: Energy per command Trend
Chart: Energy Per Command Trend Under Different Number of Subarrays
| 64 | 128 | 256 | 512 | 1024
activation energy | 1.1154 | 0.70658 | 0.50607 | 0.41361 | 0.38296
precharge energy | 1.0628 | 0.65142 | 0.44572 | 0.34287 | 0.29144
read/write energy | 3.1628 | 3.3214 | 3.6386 | 4.273 | 5.5415

## Slide 9: Bandwidth Trend

## Slide 10: Simulation Cycles Trend

## Slide 11: Latency Trend For Different Of Subarrays

## Slide 12: Write Updated Partial Refresh(WUPR)

## Slide 13: Write Updated Partial Refresh(WUPR)

## Slide 14: WUPR with 4 Segments(N=4)
Segment Pointers
Pointer Update Logic
Row Tracker
Select & Compare
SP0
SP1
SP2
SP3
r
Request
R
dref
Refresh
WUPR
refresh
dref
Ra
DRAM Row Space
N0
N1
N2
N3
SP0
SP1
SP2
SP3
Used Space
Unused Space
r

## Slide 15: WUPR Optimal Number of Segments
Simulation Configuration | 
DRAM Model | Proposed 3D-DRAM Model
Number of Banks | 64
Ideal Bandwidth | 2TB/s
Ideal Bandwidth per Core | 128GB/s
Name of Trace | Single Core Partial LLM Workload Trace
Number of Traces | 193881265
Number of Subarrays | 512
Clock Frequency | 1Ghz
DRAM Technology Node | ITRS 22nm
Selects 512 as Number of Subarray per Bank

## Slide 16: WUPR Optimal number of Segments
Find the optimal number of segments that best describe the LLM trace pattern, 16 Segments is enough
Chart: WUPR Number of Segments vs Refresh Counts
| 2 | 4 | 8 | 16 | 32 | 64 | 128
 | 59213 | 39730 | 31541 | 27451 | 27451 | 27451 | 27451
N=16

## Slide 17: Area Overhead
Chart: WUPR Area with 16nm vs Number of Segments
| 2 | 4 | 8 | 16 | 32 | 64 | 128
Area | 104.35 | 165.32 | 263.09 | 449.87 | 783.61 | 1401.34 | 2472.51
0.97% area of DRAM Controller

## Slide 18: Auto Refresh vs WUPR Settings
Simulation Configuration | 
DRAM Model | Proposed 3D-DRAM Model
Number of Banks | 64
Ideal Bandwidth | 2TB/s
Ideal Bandwidth per Core | 128GB/s
Name of Trace | Single Core Partial LLM Workload Trace
Number of Traces | 193881265
Number of Subarrays | 512
Clock Frequency | 1Ghz
Temperature Range | <85C, 85~95C, >95C
DRAM Technology Node | ITRS 22nm
Selects 512 as Number of Subarray per Bank

## Slide 19: WUPR PTPX Energy Extraction
Run a small portion of Partial LLM Simulation Workload on RTL
Spans through 512 Refreshes & Takes the Average Power calculated by PTPX
Simulation Configuration | 
DRAM Model | Proposed 3D-DRAM Model
Name of Trace | Single Core Partial LLM Workload Trace
Number of Patterns | 100000
WUPR Number of Segments | 16
Process Technology | TSMC 16nm
Clock Frequency | 1Ghz

## Slide 20: Energy Settings
Category | Description | Value
VDD | Core Supply voltage | 1.0(V)
VPP | Wordline Boost Voltage | 1.5(V)
IDD2N | Precharge Standby Current | 40(mA)
IDD3N | Active Standby Current | 55(mA)
IDD5B | Refresh Current | 250(mA)
WUPRPOWER | Average Power of WUPR | 0.5476(mW)

## Slide 21: Adding WUPR Term Into Simulator
Category | Energy Component | Formula
Command Energy | Total Activation Energy | Activation Energy (nJ/Access) × Number of Activations (nJ)
 | Total Precharge Energy | Precharge Energy (nJ/Access) × Number of Precharges (nJ)
 | Total Read Energy | Read Energy (nJ/Access) × Number of Reads (nJ)
 | Total Write Energy | Write Energy (nJ/Access) × Number of Writes (nJ)
 | Total Refresh Energy | ((VDD × IDD5B + VPP × IPP5B)× nRFCCycles × Number of Refreshes × tCKns ) / 1000 (nJ)
 | Total WUPR Energy | (WUPR Average Power × ActiveCycles × tCKns ) / 1000 (nJ)
Background Energy | Active Background Energy | ((VDD × IDD3N) + VPP × IPP3N)× ActiveCycles × tCKns ) / 1000 (nJ)
 | Idle Background Energy | ((VDD × IDD2N) + VPP × IPP2N)× IdleCycles × tCKns ) / 1000 (nJ)

## Slide 22: Energy Overhead

## Slide 23: Refresh Counts Reduction

## Slide 24: Refresh Energy Reduction

## Slide 25: Total Latency Speedup

## Slide 26: Average Bandwidth Improvements

## Slide 27: Total Energy Consumption