## Slide 1
Yeh Shun-Liang
International College of Semiconductor Technology
National Yang Ming Chiao Tung University
Weekly meeting

## Slide 2: Recent Progress
Add the description of modification to DRAM logic Die for WUPR
Analyze Refresh Counts, Average Bandwidth & Energy under different number of Subarrays per Bank

## Slide 3: Bank Analysis Configuration
Simulation Configuration | 
DRAM Model | Proposed 3D-DRAM Model
Number of Banks | 64
Ideal Bandwidth | 2TB/s
Ideal Bandwidth per Core | 128GB/s
Name of Trace | Single Core Partial LLM Workload Trace
Number of Traces | 193881265
Number of Subarrays per Bank | 32,64,128,256,512
Clock Frequency | 1Ghz
DRAM Technology Node | ITRS 32nm

## Slide 4: Timing Constraints Trend
Chart: Timing Constraints Under Different number of Subarrays
| 32 | 64 | 128 | 256 | 512
nRCD | 11 | 11 | 10 | 10 | 10
nRAS | 26 | 17 | 15 | 14 | 14
nRC | 40 | 23 | 18 | 16 | 16
nCAS | 14 | 15 | 17 | 23 | 37
nRP | 16 | 7 | 4 | 3 | 3
nRRD | 3 | 3 | 3 | 4 | 5

## Slide 5: Energy per command Trend
Chart: Energy of command with Different Number of Subarrays
| 32 | 64 | 128 | 256 | 512
Activation | 2.2514 | 1.4964 | 1.1294 | 0.96658 | 0.92671
Precharge | 2.1504 | 1.3886 | 1.0076 | 0.81719 | 0.72195
Read/Write | 5.7558 | 6.2063 | 7.1071 | 8.9081 | 12.5087

## Slide 6: DRAM Core Area Trend
Chart: DRAM Core Area Under Different Number of Subarrays
| 32 | 64 | 128 | 256 | 512
Area | 23.5591 | 24.5373 | 26.4882 | 30.3724 | 38.0955

## Slide 7: Refresh Counts with Different # of Subarrays
Chart: Refresh Counts Under Different Number of Subarrays
Auto Refresh 32 | 76574
WUPR 32 | 27445
Auto Refresh 64 | 69316
WUPR 64 | 27451
Auto Refresh 128 | 66039
WUPR 128 | 27043
Auto Refresh 256 | 65202
WUPR 256 | 27043
Auto Refresh 512 | 65202
WUPR 512 | 27043

## Slide 8: Bandwidth with Different # of Subarrays
Chart: Bandwidth Under Different Number of Subarrays
Auto Refresh 32 | 82.4621
WUPR 32 | 84.3007
Auto Refresh 64 | 91.0972
WUPR 64 | 92.9904
Auto Refresh 128 | 95.6174
WUPR 128 | 97.5051
Auto Refresh 256 | 96.8445
WUPR 256 | 98.7101
Auto Refresh 512 | 99.072
WUPR 512 | 101.4528

## Slide 9: Energy with Different # of Subarrays
Chart: Energy Consumption with Different # Of Subarrays
Auto Refresh 32 | 1239.0018
WUPR 32 | 1247.1903
Auto Refresh 64 | 1310.0524
WUPR 64 | 1303.0754
Auto Refresh 128 | 1472.5632
WUPR 128 | 1466.1739
Auto Refresh 256 | 1816.6538
WUPR 256 | 1810.4795
Auto Refresh 512 | 2513.0808
WUPR 512 | 2506.9269

## Slide 10: WUPR Architecture
Memory Controller
WUPR
Command Bus
3D DRAM Bank
DRAM Control Logic
Mode Register
DRAM rows
Refresh
Bank Control Logic
Row buffer
Row Decoder
1
2
Address
Bus
Refresh Address
3
1
Memory Controller is now in charge of recording the DRAM Bank row to refresh, address of the row to refresh has to be sent together with the Auto Refresh Command

## Slide 11: Original 3D-DRAM Die

## Slide 12: 3D-DRAM Die Modification

## Slide 13: Reference
[1] I. Bhati, Z. Chishti, S.-L. Lu, and B. L. Jacob, "Flexible Auto-Refresh: Enabling Scalable and Energy-Efficient DRAM Refresh Reductions," in Proceedings of the 42nd Annual International Symposium on Computer Architecture (ISCA), Portland, OR, USA, June 2015