## Slide 1
Yeh Shun-Liang
International College of Semiconductor Technology
National Yang Ming Chiao Tung University
Weekly meeting

## Slide 2: Recent Progress
Add the description of modification to DRAM logic Die for WUPR
Analyze Refresh Counts, Average Bandwidth & Energy under different Bank Size

## Slide 3: Bank Analysis Configuration
Simulation Configuration | 
DRAM Model | Proposed 3D-DRAM Model
Number of Banks | 64
Ideal Bandwidth | 2TB/s
Ideal Bandwidth per Core | 128GB/s
Name of Trace | Single Core Partial LLM Workload Trace
Number of Traces | 193881265
Bank Sizes | 256Mb,512Mb,1024Mb & 2048Mb
Clock Frequency | 1Ghz

## Slide 4: Timing Constraints Changes
Chart: Timing Constraints Under Different DRAM Bank Sizes
| 256Mb | 512Mb | 1024Mb | 2048Mb
nRCD | 10 | 10 | 11 | 12
nRAS | 16 | 16 | 17 | 19
nRC | 22 | 22 | 23 | 25
nCAS | 8 | 9 | 14 | 28
nRRD | 2 | 2 | 3 | 4
Chart: nRFC Under Different DRAM Bank Sizes
| 256Mb | 512Mb | 1024Mb | 2048Mb
nRFC | 60 | 80 | 110 | 160

## Slide 5: Refresh Counts with Different Bank Sizes
Chart: Auto Refresh Counts with Different DRAM Bank Sizes
| Refresh Counts
256Mb AR | 67600
512Mb AR | 67956
1024Mb AR | 69316
2048Mb AR | 70243
Worse Timing Constraints leads to longer execution time leads to more refreshes

## Slide 6: Refresh Counts with Different Bank Sizes
WUPR helps skips unnecessary refreshes thus refresh counts does not change much as bank size increases
Chart: WUPR Refresh Counts with Different DRAM Bank Sizes
| Refresh Counts
256Mb WUPR | 27450
512Mb WUPR | 27450
1024Mb WUPR | 27453
2048Mb WUPR | 27454

## Slide 7: Average Bandwidth with Different Bank Sizes
Larger banks size bank leads to longer execution time, more long period refreshes, WUPR skipping refreshes performs well for larger banks
Chart: Average Bandwidth with Different Bank Sizes
| Average Bandwidth
256Mb AR | 93.4088
256Mb WUPR | 94.5764
512Mb AR | 92.9197
512Mb WUPR | 94.3714
1024Mb AR | 91.0972
1024Mb WUPR | 92.9904
2048Mb AR | 89.8952
2048Mb WUPR | 92.512

## Slide 8: Average Bandwidth with Different Bank Sizes
Larger banks size leads to higher energy consumption due to longer latency and higher access energy
Chart: Energy Consumption Under Different Bank Sizes
| Energy Consumption
256Mb AR | 1243.9521
256Mb WUPR | 1239.9967
512Mb AR | 1245.7383
512Mb WUPR | 1240.6458
1024Mb AR | 1249.312
1024Mb WUPR | 1242.3358
2048Mb AR | 1253.9757
2048Mb WUPR | 1243.9414

## Slide 9: WUPR Architecture
Memory Controller
WUPR
Command Bus
3D DRAM Bank
Mode Register
Dummy Refresh/AR
Refresh
Management
DRAM rows
Update
Refresh
Refresh
Counter
Row buffer
Row Decoder
1
2
Bhati, I., Chishti, Z., Lu, S.-L., & Jacob, B. (2015). Flexible auto-refresh: Enabling scalable and energy-efficient DRAM refresh reductions. In Proceedings of the 42nd Annual International Symposium on Computer Architecture
2

## Slide 10: Dummy Refresh
[1] Bhati, I., Chishti, Z., Lu, S.-L., & Jacob, B. (2015). Flexible auto-refresh: Enabling scalable and energy-efficient DRAM refresh reductions. In Proceedings of the 42nd Annual International Symposium on Computer Architecture(ISCA)

## Slide 11: Original 3D-DRAM Die

## Slide 12: 3D-DRAM Die Modification

## Slide 13: Reference
[1] I. Bhati, Z. Chishti, S.-L. Lu, and B. L. Jacob, "Flexible Auto-Refresh: Enabling Scalable and Energy-Efficient DRAM Refresh Reductions," in Proceedings of the 42nd Annual International Symposium on Computer Architecture (ISCA), Portland, OR, USA, June 2015