## Slide 1
Yeh Shun-Liang
International College of Semiconductor Technology
National Yang Ming Chiao Tung University
Weekly meeting

## Slide 2: Recent Progress
Rerun the Simulation Under 22nm ITRS process node
Clarify the power model for energy calculation
Auto Refresh & WUPR Comparison

## Slide 3: Finding Optimal Number of Subarrays
Simulation Configuration | 
DRAM Model | Proposed 3D-DRAM Model
Number of Banks | 64
Ideal Bandwidth | 2TB/s
Ideal Bandwidth per Core | 128GB/s
Name of Trace | Single Core Partial LLM Workload Trace
Number of Traces | 193881265
Number of Subarrays per Bank | 64,128,256,512,1024
Clock Frequency | 1Ghz
DRAM Technology Node | ITRS 22nm

## Slide 4: Bandwidth & Simulation Latency Trend

## Slide 5: Power Model
Energy Types | Energy Component | Energy(pJ)
Command Energy | Total Activation Energy | Activation Energy (pJ/bit) × 1024(bits) × #Activations
 | Total Precharge Energy | Precharge Energy (pJ/bit) × 1024(bits) × #Precharges
 | Total Read Energy | Read Energy (pJ/bit) × 1024(bits) × #Reads
 | Total Write Energy | Write Energy (pJ/bit) × 1024(bits) × #Writes
 | Total Refresh Energy | RefreshPower× RFCCycles × #Refreshes × tCKns )
Background Energy | Active Background Energy | ((VDD(V) × IDD3N(mA)) + VPP(V) × IPP3N(mA))× ActiveCycles × tCKns )
 | Idle Background Energy | ((VDD(V) × IDD2N(mA)) + VPP(V) × IPP2N(mA))× IdleCycles × tCKns )
Voltage&Current[1] | Description | Value
VDD | Core Supply voltage | 0.9(V)
VPP | Wordline Boost Voltage | 2.3(V)
IDD2N | Precharge Standby Current | 60(mA)
IDD3N | Active Standby Current | 60(mA)
RefreshPower | Refresh Power | 155.417(mW)
[1] K. Chen, S. Li, N. Muralimanohar, J. H. Ahn, J. B. Brockman and N. P. Jouppi, "CACTI-3DD: Architecture-level modeling for 3D die-stacked DRAM main memory," 2012 Design, Automation & Test in Europe Conference & Exhibition (DATE)

## Slide 6: Energy Trend For Different Of Subarrays

## Slide 7: WUPR Optimal Number of Segments
Simulation Configuration | 
DRAM Model | Proposed 3D-DRAM Model
Number of Banks | 64
Ideal Bandwidth | 2TB/s
Ideal Bandwidth per Core | 128GB/s
Name of Trace | Single Core Partial LLM Workload Trace
Number of Traces | 193881265
Number of Subarrays per Banks | 512
Clock Frequency | 1Ghz
DRAM Technology Node | ITRS 22nm
Selects 512 as Number of Subarray per Bank

## Slide 8: WUPR with 4 Segments(N=4)
Segment Pointers
Pointer Update Logic
Row Tracker
Select & Compare
SP0
SP1
SP2
SP3
r
Request
R
dref
Refresh
WUPR
refresh
dref
Ra
DRAM Row Space
N0
N1
N2
N3
SP0
SP1
SP2
SP3
Used Space
Unused Space
r

## Slide 9: WUPR Optimal number of Segments
Find the optimal number of segments that best describe the LLM trace pattern, 16 Segments is enough
Chart: WUPR Number of Segments vs #Refreshes
| 2 | 4 | 8 | 16 | 32 | 64 | 128
 | 59213 | 39730 | 31541 | 27451 | 27451 | 27451 | 27451
N=16
Chart: WUPR Area with 16nm vs #Segments
| 2 | 4 | 8 | 16 | 32 | 64 | 128
Area | 104.35 | 165.32 | 263.09 | 449.87 | 783.61 | 1401.34 | 2472.51
0.97% Area of DRAM Controller

## Slide 10: WUPR Analysis Settings
Simulation Configuration | 
DRAM Model | Proposed 3D-DRAM Model
Number of Banks | 64
Ideal Bandwidth | 2TB/s
Ideal Bandwidth per Core | 128GB/s
Name of Trace | Single Core Partial LLM Workload Trace
Number of Traces | 193881265
Number of Subarrays per Bank | 512
WUPR Number of Segments | 16
Clock Frequency | 1Ghz
Temperature Range | <85C, 85~95C, >95C
DRAM Technology Node | ITRS 22nm
Logic Technology | TSMC 16nm
Selects 16 as the Number of Segment for WUPR

## Slide 11: WUPR PTPX Energy Extraction
Simulation Configuration | 
DRAM Model | Proposed 3D-DRAM Model
Name of Trace | Single Core Partial LLM Workload Trace
Number of Patterns | 100000
WUPR Number of Segments | 16
Logic Process Technology | TSMC 16nm
Clock Frequency | 1Ghz
To span through 512 Refreshes, takes a portion of Partial LLM Workload Trace & Calculate Average Power using PTPX for WUPR, add to Power Model

## Slide 12
Energy Types | Energy Component | Energy(pJ)
Command Energy | Total Activation Energy | ActivationPower × RASCycles × #Activations × tCKns
 | Total Precharge Energy | × #Precharges
 | Total Read Energy | × #Reads
 | Total Write Energy | × #Writes
 | Total Refresh Energy | RefreshPower(mW) * RFCCycles × #Refreshes × tCKns
 | Total WUPR Energy | (WUPR Average Power(mW) × (IdleCycles+ActiveCycles )× tCKns )
Background Energy | Active Background Energy | ((VDD(V) × IDD3N(mA)) + VPP(V) × IPP3N(mA))× ActiveCycles × tCKns )
 | Idle Background Energy | ((VDD(V) × IDD2N(mA)) + VPP(V) × IPP2N(mA))× IdleCycles × tCKns )
Voltage&Current[2] | Description | Value
VDD | Core Supply voltage | 0.9(V)
VPP | Wordline Boost Voltage | 2.3(V)
IDD2N | Precharge Standby Current | 60(mA)
IDD3N | Active Standby Current | 60(mA)
WUPRPOWER | Average Power of WUPR | 0.5476(mW)
Command Power | Description | P
Read | Read Power | 754.052
Write | Write Power | 452.432
Activate | Activate Power | 10.98
Precharge | Precharge Power | 8.73
Refresh | Refresh Power | 155.417
Command Power | Description | 
Read | Read Power | 754.052
Write | Write Power | 452.432
Activate | Activate Power | 10.98
Precharge | Precharge Power | 8.73
Refresh | Refresh Power | 155.417
[1] K. Chen, S. Li, N. Muralimanohar, J. H. Ahn, J. B. Brockman and N. P. Jouppi, "CACTI-3DD: Architecture-level modeling for 3D die-stacked DRAM main memory," 2012 Design, Automation & Test in Europe Conference & Exhibition (DATE)

## Slide 13: Refresh Counts & Energy Reduction

## Slide 14: Total Energy Consumption

## Slide 15: References
[2] K. Chen, S. Li, N. Muralimanohar, J. H. Ahn, J. B. Brockman and N. P. Jouppi, "CACTI-3DD: Architecture-level modeling for 3D die-stacked DRAM main memory," 2012 Design, Automation & Test in Europe Conference & Exhibition (DATE)
[1] JEDEC Solid State Technology Association, High Bandwidth Memory (HBM) DRAM, JESD235D, Oct. 2020

## Slide 16: Appendices(Timing Constraints Trend)
Chart: Timing Constraints Trend Under Different number of Subarrays
| 64 | 128 | 256 | 512 | 1024
nRCD | 8 | 7 | 7 | 7 | 6
nRAS | 30 | 16 | 12 | 10 | 10
nRC | 52 | 24 | 15 | 12 | 12
nCAS | 5 | 6 | 8 | 13 | 23
nRP | 23 | 9 | 5 | 3 | 2
nRRD | 2 | 3 | 3 | 3 | 4

## Slide 17: Write Updated Partial Refresh(WUPR)

## Slide 18: Write Updated Partial Refresh(WUPR)

## Slide 19: Timing Constraints Trend
Chart: Timing Constraints Trend Under Different number of Subarrays
| 64 | 128 | 256 | 512 | 1024
nRCD | 8 | 7 | 7 | 7 | 6
nRAS | 30 | 16 | 12 | 10 | 10
nRC | 52 | 24 | 15 | 12 | 12
nCAS | 5 | 6 | 8 | 13 | 23
nRP | 23 | 9 | 5 | 3 | 2
nRRD | 2 | 3 | 3 | 3 | 4

## Slide 20: Energy per command Trend
Chart: Energy Per Command Trend Under Different Number of Subarrays
| 64 | 128 | 256 | 512 | 1024
activation energy | 1.1154 | 0.70658 | 0.50607 | 0.41361 | 0.38296
precharge energy | 1.0628 | 0.65142 | 0.44572 | 0.34287 | 0.29144
read/write energy | 3.1628 | 3.3214 | 3.6386 | 4.273 | 5.5415

## Slide 21: Total Latency Speedup

## Slide 22: Average Bandwidth Improvements

## Slide 23: Total Energy Consumption

## Slide 24: Energy Trend For Different Of Subarrays

## Slide 25: Bandwidth & Simulation Latency Trend